## Slide 1: HARR Algoritm
Heart and respiration rate detection with accelerometer

## Slide 2: The Problem
Find an alternative way to know your heart rate and respiratory rate using the technologies made available by modern smartphones

## Slide 3: The accelerometer
The accelerometer is a device that measures the accelerations of the object on which it is placed along the three axes x, y and z

## Slide 4: The idea
Place the phone on your chest in a supine position Record micro chest movements with the accelerometer Analyze the signal Get your heart and breathing rate

## Slide 5: Data collection
Android application to collect accelerometer data
Finger oximeter for heartbeat

## Slide 6: Observations
During a breathing cycle (inhale + exhale) The Z-axis increases and decreases evenly and steadily over time.
During a heartbeat, the x-axis rises and falls suddenly, generating spikes.
I Two phenomena of breathing and pulsation influence each other, affecting both the axes.

## Slide 7: The Algorithm
1. Upload the CSV file 2. Read Data in a correct manner 3. Extract accelerometer data along the x, y, and z axes 4. Filter data: - Applies a low-pass filter to accelerometer data along the z-axis - Applies a bandpass filter to accelerometer data along the x-axis 5. Calculate the Fourier Transform: - Calculate frequencies - Calculate the Fourier transform of accelerometer data along the axis - Calculate the amplitude spectrum of the signal
6. Detect respiratory spikes on the obtained signal along the Z-axis 7. Detect Heart Spikes on the obtained signal along the X-Axis 8. Calculate the breathing rate in bpm (breath par minute) 9. Calculate the heart rate in bpm (beats par minute)

## Slide 8: Low-pass filter
Low-pass filtering can be used to remove high-frequency noise from a signal, allowing only the relevant low-frequency components

## Slide 9: Bandpass filter
The bandpass filter is used to extract specific frequency components from a signal, eliminating both high and low frequency components

## Slide 10: filter

## Slide 11: Fourier transform
The application of the Fourier Transform (FFT) in this context of analyzes accelerometer data is to identifie the frequency components associated with breathing and heartbeats and is also used to filter out unwanted frequencies in the signal, for example by eliminating frequencies associated with noise or unwanted movements.

## Slide 12: Calculation of respiratory and heart rate

## Slide 13
Searching for peaks in the filtered signal Calculate the period between two peaks Calculate the frequency as the period multiplied by 60 divided by the duration of the signal
90 BPM
(beats per minute)
30 BPM
(breaths per minute)

## Slide 14: Results
Testing:
-10 subjects -2 tasks -100 recordings
Influencing factors: -Influence of the heartbeat -Positioning of the smartphone -Smartphone movements
60% accuratezza
Parameters: - fs: Sampling Rate - duration: Duration of the signal - n: Signal length - f_cutoff_resp: Cut-off frequency of the low-pass filter - f_cutoff_heart_low: Cutoff frequency lower bandpass filter - f_cutoff_heart_high: Cutoff frequency upper bandpass filter

## Slide 15: Conclusions
Test the algorithm on a larger, more evenly distributed dataset. The algorithm is not 100% reliable, it depends a lot on how the phone is placed and the movements of the body during signal recording. In the future, to improve performance, this algorithm could be thought of as a signal pre-processing step to be used as a feauture of a neural network.

## Slide 16: In the future, it will be the small Things to Make the Big Changes